## Slide 1: AARCH64 Floating Point

## Slide 2: Registers
32 floating point registers
Bn – 8 bit
Hn – 16 bit
Sn – 32 bit
Dn – 64 bit
Qn – 128 bit

## Slide 3: Single Precision Format – IEEE 754
±1.18×10^−38 to ±3.4×10^38
1 bit sign for fraction sign is 0 so result is positive
8 bit mantissa offset by 127 7C – 7F = 0xFFFFFFFFFFFFFFFD -> 2’s complement == 3
23 bit fraction 1.25 – the 1 is implicit

## Slide 4: Double Precision Format – IEEE 754
±2.23×10^−308 to ±1.80×10^308
1 bit sign for fraction
11 bit exponent – offset by 1024
52 bit fraction

## Slide 5: Float constants are not straight forward
float single() {
return 1.2345678;
}
single:
mov w0, 1617
movk w0, 0x3f9e, lsl 16
fmov s0, w0
ret

## Slide 6: Double constants are not straight forward
double duble() {
return 1.234567890123456;
}
duble:
adrp x0, .LC0
ldr d0, [x0, #:lo12:.LC0]
ret
.LC0: // in .data
.word 1116494328
.word 1072939210